- Introduction
  - Least Squares for Polynomial Regression
  - Least Square for Multi-Image Geopositioning (MIG)
  - Output covariance, reference variance
  - What happens to ocov as N increases
- Experimental Results
  - Data Amplification
  - Methodology
  - Results

---
Least Squares Line Fitting
Solve for m,b that minimize
y
x
\sum r_i^2
y=mx+b
(x_i,y_i)
y_p=mx_i+b
r_i=y_i-y_p

---
Least Squares Line Fitting
- Use initial guess of m,b to compute ri
- What Dm,Db best fulfills the residuals?
- Solution of overdetermined linear system:
\begin{eqnarray*} x_1m+b&=&r_1\\ x_2m+b&=&r_2\\ \vdots&&\\ x_nm+b&=&r_n \end{eqnarray*}

---
Least Squares Line Fitting
- Use initial guess of m,b to compute ri
- What Dm,Db best fulfills the residuals?
- Solution of overdetermined linear system:
\begin{bmatrix} x_1 & 1\\ x_2 & 1\\ \vdots & \vdots\\ x_n & 1 \end{bmatrix} \begin{bmatrix} \Delta m\\ \Delta b \end{bmatrix} = \begin{bmatrix} r_1\\ r_2\\ \vdots\\ r_n\\ \end{bmatrix}

---
Least Squares Line Fitting
- Use initial guess of m,b to compute ri
- What Dm,Db best fulfills the residuals?
- Solution of overdetermined linear system:
\begin{eqnarray*} A\Delta&=&r\\ \Delta&=&(A'A)^{-1}A'r \end{eqnarray*}

---
Least Squares Line Fitting
(3,5)
2
(2,3)
1
(1,2)
1
y=1x+0
\begin{eqnarray*} \begin{bmatrix} 1 & 1\\ 2 & 1\\ 3 & 1 \end{bmatrix} \begin{bmatrix} \Delta m\\ \Delta b \end{bmatrix} &=& \begin{bmatrix} 1\\ 1\\ 2\\ \end{bmatrix} \\ A\Delta &=& r \\ \Delta &=& (A'A)^{-1}A'r \end{eqnarray*}

---
Least Squares Line Fitting
(3,5)
2
(2,3)
1
(1,2)
1
y=1x+0
\begin{eqnarray*} \begin{bmatrix} 1 & 1\\ 2 & 1\\ 3 & 1 \end{bmatrix} \begin{bmatrix} \Delta m\\ \Delta b \end{bmatrix} &=& \begin{bmatrix} 1\\ 1\\ 2\\ \end{bmatrix} \\ A\Delta &=& r \\ \Delta &=& (A'A)^{-1}A'r \\ \Delta &=& \begin{bmatrix} 1/2\\ 1/3 \end{bmatrix} \\

---
Least Squares Line Fitting
y=1.5x+0.\overline{3}
y=1x+0
\begin{eqnarray*} \begin{bmatrix} 1 & 1\\ 2 & 1\\ 3 & 1 \end{bmatrix} \begin{bmatrix} \Delta m\\ \Delta b \end{bmatrix} &=& \begin{bmatrix} 1\\ 1\\ 2\\ \end{bmatrix} \\ A\Delta &=& r \\ \Delta &=& (A'A)^{-1}A'r \\ \Delta &=& \begin{bmatrix} 1/2\\ 1/3 \end{bmatrix} \\

---
Least Squares Polynomial Fitting
The principle can be extended beyond linear:
\begin{eqnarray*} x_1m+b&=&r_1\\ x_2m+b&=&r_2\\ \vdots&&\\ x_nm+b&=&r_n \end{eqnarray*}
\begin{bmatrix} x_1 & 1\\ x_2 & 1\\ \vdots & \vdots\\ x_n & 1 \end{bmatrix} \begin{bmatrix} \Delta m\\ \Delta b \end{bmatrix} = \begin{bmatrix} r_1\\ r_2\\ \vdots\\ r_n\\ \end{bmatrix}
\begin{eqnarray*} A\Delta&=&r\\ \Delta&=&(A'A)^{-1}A'r \end{eqnarray*}
f(x)=mx+b

---
Least Squares Polynomial Fitting
The principle can be extended beyond linear:
\begin{eqnarray*} x_1^2a_2+x_1a_1+a_0&=&r_1\\ x_2^2a_2+x_2a_1+a_0&=&r_1\\ \vdots&&\\ x_n^2a_2+x_na_1+a_0&=&r_1\\ \end{eqnarray*}
\begin{bmatrix} x_1^2 & x_1 & 1\\ x_2^2 & x_2 & 1\\ \vdots & \vdots\\ x_n^2 & x_n & 1 \end{bmatrix} \begin{bmatrix} \Delta a_2\\ \Delta a_1\\ \Delta a_0 \end{bmatrix} = \begin{bmatrix} r_1\\ r_2\\ \vdots\\ r_n\\ \end{bmatrix}
\begin{eqnarray*} A\Delta&=&r\\ \Delta&=&(A'A)^{-1}A'r \end{eqnarray*}
f(x)=a_2x^2+a_1x+a_0

---
Least Squares Polynomial Fitting
The principle can be extended beyond linear:
\begin{eqnarray*} x_1^2a_2+x_1a_1+a_0&=&r_1\\ x_2^2a_2+x_2a_1+a_0&=&r_1\\ \vdots&&\\ x_n^2a_2+x_na_1+a_0&=&r_1\\ \end{eqnarray*}
\begin{bmatrix} \frac{\partial f(x_1)}{\partial a_2}& \frac{\partial f(x_1)}{\partial a_1} & \frac{\partial f(x_1)}{\partial a_0}\\ \frac{\partial f(x_2)}{\partial a_2}& \frac{\partial f(x_2)}{\partial a_1} & \frac{\partial f(x_2)}{\partial a_0}\\ & \vdots&\\ \frac{\partial f(x_n)}{\partial a_2}& \frac{\partial f(x_n)}{\partial a_1} & \frac{\partial f(x_n)}{\partial a_0}\\ \end{bmatrix} \begin{bmatrix} \Delta a_2\\ \Delta a_1\\ \Delta a_0 \end{bmatrix} = \begin{bmatrix} r_1\\ r_2\\ \vdots\\ r_n\\ \end{bmatrix}
\begin{eqnarray*} A\Delta&=&r\\ \Delta&=&(A'A)^{-1}A'r \end{eqnarray*}
f(x)=a_2x^2+a_1x+a_0

---
Least Squares Polynomial Fitting
The principle can be extended to general functions:
\begin{bmatrix} \frac{\partial f(x_1)}{\partial a_1}& \frac{\partial f(x_1)}{\partial a_2} &\ldots& \frac{\partial f(x_1)}{\partial a_m}\\ \frac{\partial f(x_2)}{\partial a_1}& \frac{\partial f(x_2)}{\partial a_2} & \ldots&\frac{\partial f(x_2)}{\partial a_m}\\ & \vdots&\\ \frac{\partial f(x_n)}{\partial a_1}& \frac{\partial f(x_n)}{\partial a_2} & \ldots&\frac{\partial f(x_n)}{\partial a_m}\\ \end{bmatrix} \begin{bmatrix} \Delta a_1\\ \Delta a_2\\ \vdots\\ \Delta a_m \end{bmatrix} = \begin{bmatrix} r_1\\ r_2\\ \vdots\\ r_n\\ \end{bmatrix}
\begin{eqnarray*} A\Delta&=&r\\ \Delta&=&(A'A)^{-1}A'r \end{eqnarray*}
f(x|a_1,a_2,...a_m)=???

---
Weighted Least Squares
- <repeat previous example with error bars>
- <large sigma allows large residual, line can be far from outliers>
- <small sigma penalizes large residual, line forced nearer to outliers>
\begin{eqnarray*} W= \begin{bmatrix} \frac{1}{\sigma_1^2} & & & \\ & \frac{1}{\sigma_2^2} & & \\ & & \ddots & \\ & & & \frac{1}{\sigma_n^2} \end{bmatrix}\\ \Delta = (A'WA)^{-1}A'Wr \end{eqnarray*}

---
Multi-Image Geopositioning
- show 3 frames, non-intersrecting rays
- show candidate ground point
- show projection into images, residuals
- g2i(x,y,z)=(r,c)
- Paste sm101 slides for numerical ground partials?
- Show A\Delta g=r filled with gparts and resids
- Diagonalize/decompose (now or later?)
- Draw meas err circles add W to equations
- Draw “wiggled” image rays, reproject to increase meas err circles
- gparts nonlinear, need to iterate

---
Output Covariance
- inv(A'WA) is output covariance (predicted error)
  - Estimate of accuracy of solved answer
  - Depends on meas sigmas, sensor parameter sigmas, collection geometry
  - Visualize diagonal with sigmas in 3 dimensions
  - Visualize non-diagonal with sigmas=evals along 3 evecs
- Reference variance (paste goldilocks, mama/papa bears)
  - >>1 if distribution of resids too large for W
  - <<1 if distribution of resids too small for W
  - ~1 if just right

---
Combining Weight/Covariance
- Start with one nadir ray, image error
- Ray is Z axis; ground partials X/Y axes
- With just one ray, the least squares system under-determined!
  - 2 equations, 3 unknowns
C=\begin{bmatrix}\sigma^2 & 0\\0 & \sigma^2\end{bmatrix}; W=\begin{bmatrix}1/\sigma^2 & 0\\0 & 1/\sigma^2\end{bmatrix}

---
Combining Weight/Covariance
- “Ellipsoid” is vertical cylinder
\begin{eqnarray*} W_Z &=& \begin{bmatrix}1&0\\0&1\\0&0\end{bmatrix} \begin{bmatrix}1/\sigma^2 &0 \\ 0&1/\sigma^2 \end{bmatrix} \begin{bmatrix}1&0&0\\0&1&0\end{bmatrix}\\ &=&\begin{bmatrix}1/\sigma^2&0&0 \\ 0& 1/\sigma^2 &0 \\ 0&0&0\end{bmatrix}\\ C_Z & = & \begin{bmatrix}\sigma^2&0&0 \\ 0& \sigma^2 &0 \\ 0&0&\infty\end{bmatrix} \end{eqnarray*}

---
Combining Weight/Covariance
- Add a second image ray along the X axis
- Error “ellipsoid” is horizontal cylinder
\begin{eqnarray*} W_X &=& \begin{bmatrix}0&0\\1&0\\0&1\end{bmatrix} \begin{bmatrix}1/\sigma^2 &0 \\ 0&1/\sigma^2 \end{bmatrix} \begin{bmatrix}0&1&0\\0&0&1\end{bmatrix}\\ &=&\begin{bmatrix}0&0&0 \\ 0& 1/\sigma^2&0 \\ 0&0& 1/\sigma^2 \\ \end{bmatrix}\\ C_X & = & \begin{bmatrix}\infty&0&0\\ 0&\sigma^2&0 \\ 0&0& \sigma^2\end{bmatrix} \end{eqnarray*}

---
Combining Weight/Covariance
- Combine both rays in a MIG
- Ellipsoid shape:
  - X/Z radii
  - Y radius
\begin{eqnarray*} W_{ZX}&=& \begin{bmatrix}1/\sigma^2&0&0 \\ 0& 1/\sigma^2&0 \\ 0&0& 0 \end{bmatrix} +\begin{bmatrix}0&0&0 \\ 0& 1/\sigma^2&0 \\ 0&0& 1/\sigma^2 \end{bmatrix}\\ &=&\begin{bmatrix}1/\sigma^2&0&0 \\ 0& 2/\sigma^2&0 \\ 0&0& 1/\sigma^2 \end{bmatrix}\\ C_{ZX} & = & \begin{bmatrix}\sigma^2&0&0\\ 0&\sigma^2/2&0 \\ 0&0& \sigma^2\end{bmatrix} \end{eqnarray*}
=\sigma/\sqrt{2}
=\sigma

---
Combining Weight/Covariance
- Add a 3rd ray along Y axis
- Ellipsoid is spherical
  - All radii are
\begin{eqnarray*} W_{ZXY}&=& \begin{bmatrix}2/\sigma^2&0&0 \\ 0& 2/\sigma^2&0 \\ 0&0& 2/\sigma^2 \end{bmatrix}\\ C_{ZXY} & = & \begin{bmatrix}\sigma^2/2&0&0\\ 0&\sigma^2/2&0 \\ 0&0& \sigma^2/2\end{bmatrix} \end{eqnarray*}
\sigma/\sqrt{2}

---
Combining Weight/Covariance
- Each additional ray reduces uncertainty two directions orthogonal to it
  - Lots of near-nadir images→lots of vertical uncertainty
  - Near-horizontal rays all around→horizontal uncertainty
  - Photogrammetry is mostly overhead→generally more vertical uncertainty
- Calculation of Cg independent of ray separation!
  - Purely a function of relative geometry of rays
  - Refvar measures how well Cg predicts ground accuracy
- #weights 1→2 ==> var s2→s2/2 ==> sig s→s/sqrt(2)
  - Law of Large Numbers/Central Limit Theorem
  - Average of N samples has accuracy ~ 1/sqrt(N)

---
Data Amplification
- Start with 10 overlapping Worldview-1 images
  - 5 stereo pairs, gsd~0.5m
  - Dolloff, Settergren tinyurl.com/MIN_ASPRS2010
  - Neighborhood of 36N 117.5W (footprints, point)
    - ~UTM11N 455000 3984000 1700
  - Graph of 10 look vectors (labeled with image ids?)
- Perturb adjustable parameters (pos, att, vel, etc) to obtain 99 variants per original-->1000 images
- Choose ground point, project to 1000 image points
  - “Truth” = perfect 1000-image ray intersection
- Further perturb 1000 images with controlled error per parameter
  - “Error” = 1000-image rays that don't intersect

---
Methodology
- For N=4...1000
  - For K=1...100
    - Randomly sample subset of N images
    - Compute MIG
      - MIG-truth = measured error
      - Output covariance = predicted error
- Analyze
  - Refvars~1?
  - Do measured errors fit predictions?
  - Distribution of measured errors as N grows large?

---
Results
- Refvars~1, clustering tighter as N+++
- Distribution of meas errors matches prediction (20%, 90%, 95%, 99% ellipsoid statistics)
- Horizontal, vertical errors decrease as N+++
  - Err/sqrt(N) is linear

---
Variations
- Increased measurement error
  - Refvar still ~1, still matches predictions, still ~1/sqrt(N)
  - Increased ground error
- Variable sensor error (x1-->x5)
  - Refvar still ~1, still matches predictions, still ~1/sqrt(N)
  - Increased ground error
- Half/Quarter Cones
  - Refvar still ~1, still matches predictions, still ~1/sqrt(N)
  - Vertical error increases with decreased convergence angle
  - Horizontal error: half~less, but quarter~way more?

---
Conclusion
Mo images mo betta