Title here

---
Outline
Duplicated 3-4 times as placeholder

---
Multi-Image Geopositioning (MIG)
Seth MIG stuff here

---
Multi-Image Geopositioning
- Multiple overhead images see a ground feature
- If we know position/orientation/etc, we can triangulate the location of the ground feature

---
Multi-Image Geopositioning
- Multiple overhead images see a ground feature
- If we know position/orientation/etc, we can triangulate the location of the ground feature

---
Multi-Image Geopositioning
- In reality, position/orientation/etc are imperfect estimates
- Rays do not intersect!
  - Location of ground feature cannot be known certainly
  - Need to find ground point “closest to all” rays

---
Multi-Image Geopositioning
- “Sensor Model” functions map between ground/image
  - Ground-to-image (g2i), Image-to-ground (i2g) are inverses
- Many (infinite) ground points map to each image point
  - Image rays are all (x,y,z) that g2i map to the same (r,c)
  - Equivalent: i2g(r,c,z) for all z
\begin{eqnarray*} (r,c)&=&g2i(x,y,z)\\ & \Leftrightarrow& \\ (x,y)&=&i2g(r,c,z) \end{eqnarray*}

---
Multi-Image Geopositioning
- Project initial ground point into all images with g2i
- Adjust the position of the ground point to minimize the sum of squares of image residuals
rc
rr
\Sigma (rr^2+rc^2)

---
Multi-Image Geopositioning
The optimal ground point correction is found by solving the normal equations:
rc
rr
Corrections to ground point estimate
B'WB\Delta=B'W\pmb{f}

---
Multi-Image Geopositioning
The ground point uncertainty for N images is given by:
rc
rr
3x3 ground point covariance matrix
2Nx3 ground partials
Sensor parameter partials
2Nx2N weight matrix
Measurement weight matrix
Sensor parameter weight matrix
C^g = (B'WB)^{-1}
W = (W^{x^{-1}}+AW^{p^{-1}}A')^{-1}

---
Multi-Image Geopositioning (MIG)
- How does depend on the number of images N?
- Assumptions:
  - Image measurements are uncorrelated
  - Sensor parameters from different images are uncorrelated
  - Image measurement rays are not parallel
C^g

---
Multi-Image Geopositioning (MIG)
- How does depend on the number of images N?
- If are the three eigenvalues of
C^g
\lambda_1 \leq \lambda_2 \leq \lambda_3 \leq \frac{2}{(N-1)\delta}
{\lambda_1, \lambda_2, \lambda_3}
C^g
\delta > 0
\delta
   is a determined by the system. A positive value ensures not all measurement rays are parallel

---
Multi-Image Geopositioning (MIG)
- How does depend on the number of images N?
- The eigenvalues of are the variances of ground uncertainty in the directions of the three axes
C^g
\lambda_1 \leq \lambda_2 \leq \lambda_3 \leq \frac{2}{(N-1)\delta}
C^g

---
Multi-Image Geopositioning (MIG)
- How does depend on the number of images N?
- Assume image measurements and sensor parameters from different images are uncorrelated
C^g
\begin{eqnarray*} B'WB & = & \sum_{i}^NB'_i(W^{m^{-1}}_i + A_iW^{p^{-1}}A'_i)^{-1}B_i \\ & = & \sum_{i}^NB'_iW_iB_i \end{eqnarray*}

---
Multi-Image Geopositioning (MIG)
It can be shown that for a strictly positive parameter <delta> the smallest eigenvalue of
\lambda_1(\sum_{i}^NB'_iW_iB_i) \geq \frac{(N-1)\delta}{2}

---
Data Synthesis
- Start with 10 overlapping Worldview-1 images
  - 5 stereo pairs, GSD~0.5m
  - Common overlap area includes 36N 117.5W
  - Dolloff, Settergren, ASPRS 2010
- Perturb adjustable parameters (pos, att, vel, etc)
  - 99 variants per original→1000 images
- Choose ground point, project to 1000 image points
  - UTM11N 455000 3984000 1700
  - “Truth” = perfect 1000-image ray intersection
- Further perturb 1000 images
  - Each parameter perturbation randomly sampled Normal with controlled sigma
  - “Error” = 1000 image rays that don't intersect

---
Original 10 Images

---
Data Amplification
- <original 10 look vectors>
- <original 1000 look vectors>
- <perturbed 1000 hi intersections>

---
Methodology
- For N=4...1000
  - For K=1...100
    - Randomly sample subset of N images
    - Compute MIG
      - MIG - truth = measured error
      - Output covariance = predicted error
      - Reference variance = self-consistency check
- Analyze
  - What is the distribution of errors as N grows large?
  - Are reference variances ~ 1?
  - Do measured errors fit predictions (Cout)?

---
Use charts from paper

---
Hourglassin

---
More charts