Outline
- Introduction
  - Least squares for polynomial regression
  - Least squares for Multi-Image Geopositioning (MIG)
  - Improved accuracy with increasing number of images
- Experimental Results
  - Data synthesis, Methodology
  - Results
- Conclusion

---
Outline
- Introduction
  - Least squares for polynomial regression
  - Least squares for Multi-Image Geopositioning (MIG)
  - Improved accuracy with increasing number of images
- Experimental Results
  - Data synthesis, Methodology
  - Results
- Conclusion

---
Least Squares Line Fitting
Solve for m,b that minimize
y
x
\sum r_i^2
y=mx+b
(x_i,y_i)
y_p=mx_i+b
r_i=y_i-y_p

---
Least Squares Line Fitting
- Use initial guess of m,b to compute ri
- What Dm,Db best fulfills the residuals?
- Solution of overdetermined linear system:
\begin{eqnarray*} x_1\Delta m+\Delta b&=&r_1\\ x_2\Delta m+\Delta b&=&r_2\\ \vdots&&\\ x_n\Delta m+\Delta b&=&r_n \end{eqnarray*}

---
Least Squares Line Fitting
- Use initial guess of m,b to compute ri
- What Dm,Db best fulfills the residuals?
- Solution of overdetermined linear system:
\begin{bmatrix} x_1 & 1\\ x_2 & 1\\ \vdots & \vdots\\ x_n & 1 \end{bmatrix} \begin{bmatrix} \Delta m\\ \Delta b \end{bmatrix} = \begin{bmatrix} r_1\\ r_2\\ \vdots\\ r_n\\ \end{bmatrix}

---
Least Squares Line Fitting
- Use initial guess of m,b to compute ri
- What Dm,Db best fulfills the residuals?
- Solution of overdetermined linear system:
\begin{eqnarray*} A\Delta&=&r\\ \vdots&&\\ \Delta&=&(A'A)^{-1}A'r \end{eqnarray*}

---
Least Squares Line Fitting
(3,5)
2
(2,3)
1
(1,2)
1
y=1x+0
\begin{eqnarray*} \begin{bmatrix} 1 & 1\\ 2 & 1\\ 3 & 1 \end{bmatrix} \begin{bmatrix} \Delta m\\ \Delta b \end{bmatrix} &=& \begin{bmatrix} 1\\ 1\\ 2\\ \end{bmatrix} \\ A\Delta &=& r \\ \Delta &=& (A'A)^{-1}A'r \end{eqnarray*}

---
Least Squares Line Fitting
(3,5)
2
(2,3)
1
(1,2)
1
y=1x+0
\begin{eqnarray*} \begin{bmatrix} 1 & 1\\ 2 & 1\\ 3 & 1 \end{bmatrix} \begin{bmatrix} \Delta m\\ \Delta b \end{bmatrix} &=& \begin{bmatrix} 1\\ 1\\ 2\\ \end{bmatrix} \\ A\Delta &=& r \\ \Delta &=& (A'A)^{-1}A'r \\ \begin{bmatrix} \Delta m\\ \Delta b \end{bmatrix}&=& \begin{bmatrix} 1/2\\ 1/3 \end{bmatrix} \\

---
Least Squares Line Fitting
y=1.5x+0.\overline{3}
y=1x+0
\begin{eqnarray*} \begin{bmatrix} 1 & 1\\ 2 & 1\\ 3 & 1 \end{bmatrix} \begin{bmatrix} \Delta m\\ \Delta b \end{bmatrix} &=& \begin{bmatrix} 1\\ 1\\ 2\\ \end{bmatrix} \\ A\Delta &=& r \\ \Delta &=& (A'A)^{-1}A'r \\ \begin{bmatrix} \Delta m\\ \Delta b \end{bmatrix}&=& \begin{bmatrix} 1/2\\ 1/3 \end{bmatrix} \\

---
Least Squares Polynomial Fitting
The principle can be extended beyond linear:
\begin{bmatrix} x_1 & 1\\ x_2 & 1\\ \vdots & \vdots\\ x_n & 1 \end{bmatrix} \begin{bmatrix} \Delta m\\ \Delta b \end{bmatrix} = \begin{bmatrix} r_1\\ r_2\\ \vdots\\ r_n\\ \end{bmatrix}
\begin{eqnarray*} A\Delta&=&r\\ \Delta&=&(A'A)^{-1}A'r \end{eqnarray*}
f(x)=mx+b
\begin{eqnarray*} x_1\Delta m+\Delta b&=&r_1\\ x_2\Delta m+\Delta b&=&r_2\\ \vdots&&\\ x_n\Delta m+\Delta b&=&r_n \end{eqnarray*}

---
Least Squares Polynomial Fitting
The principle can be extended beyond linear:
\begin{eqnarray*} x_1^2\Delta a_2+x_1\Delta a_1+\Delta a_0&=&r_1\\ x_2^2\Delta a_2+x_2\Delta a_1+\Delta a_0&=&r_1\\ \vdots&&\\ x_n^2\Delta a_2+x_n\Delta a_1+\Delta a_0&=&r_1\\ \end{eqnarray*}
\begin{bmatrix} x_1^2 & x_1 & 1\\ x_2^2 & x_2 & 1\\ & \vdots\\ x_n^2 & x_n & 1 \end{bmatrix} \begin{bmatrix} \Delta a_2\\ \Delta a_1\\ \Delta a_0 \end{bmatrix} = \begin{bmatrix} r_1\\ r_2\\ \vdots\\ r_n\\ \end{bmatrix}
\begin{eqnarray*} A\Delta&=&r\\ \Delta&=&(A'A)^{-1}A'r \end{eqnarray*}
f(x)=a_2x^2 + a_1x + a_0

---
Least Squares Polynomial Fitting
The principle can be extended beyond linear:
\begin{bmatrix} \frac{\partial f(x_1)}{\partial a_2}& \frac{\partial f(x_1)}{\partial a_1} & \frac{\partial f(x_1)}{\partial a_0}\\ \frac{\partial f(x_2)}{\partial a_2}& \frac{\partial f(x_2)}{\partial a_1} & \frac{\partial f(x_2)}{\partial a_0}\\ & \vdots&\\ \frac{\partial f(x_n)}{\partial a_2}& \frac{\partial f(x_n)}{\partial a_1} & \frac{\partial f(x_n)}{\partial a_0}\\ \end{bmatrix} \begin{bmatrix} \Delta a_2\\ \Delta a_1\\ \Delta a_0 \end{bmatrix} = \begin{bmatrix} r_1\\ r_2\\ \vdots\\ r_n\\ \end{bmatrix}
\begin{eqnarray*} A\Delta&=&r\\ \Delta&=&(A'A)^{-1}A'r \end{eqnarray*}
f(x)=a_2x^2+a_1x+a_0
\begin{eqnarray*} x_1^2\Delta a_2+x_1\Delta a_1+\Delta a_0&=&r_1\\ x_2^2\Delta a_2+x_2\Delta a_1+\Delta a_0&=&r_1\\ \vdots&&\\ x_n^2\Delta a_2+x_n\Delta a_1+\Delta a_0&=&r_1\\ \end{eqnarray*}

---
Least Squares Polynomial Fitting
The principle can be extended to general functions:
\begin{bmatrix} \frac{\partial f(x_1)}{\partial a_1}& \frac{\partial f(x_1)}{\partial a_2} &\ldots& \frac{\partial f(x_1)}{\partial a_m}\\ \frac{\partial f(x_2)}{\partial a_1}& \frac{\partial f(x_2)}{\partial a_2} & \ldots&\frac{\partial f(x_2)}{\partial a_m}\\ & \vdots&\\ \frac{\partial f(x_n)}{\partial a_1}& \frac{\partial f(x_n)}{\partial a_2} & \ldots&\frac{\partial f(x_n)}{\partial a_m}\\ \end{bmatrix} \begin{bmatrix} \Delta a_1\\ \Delta a_2\\ \vdots\\ \Delta a_m \end{bmatrix} = \begin{bmatrix} r_1\\ r_2\\ \vdots\\ r_n\\ \end{bmatrix}
\begin{eqnarray*} A\Delta&=&r\\ \Delta&=&(A'A)^{-1}A'r \end{eqnarray*}
f(x|a_1,a_2,...a_m)=???

---
Weighted Least Squares
- Consider adding error bars
- “Unweighted” solution?
  - All observations weighted
  - Note diagonal W-1 and W pull through as scalars and cancel
\pm\sigma_i
\begin{eqnarray*} Cov_i&=&\sigma_i^2\\ W&=& \begin{bmatrix} \frac{1}{\sigma_1^2} & & & \\ & \frac{1}{\sigma_2^2} & & \\ & & \ddots & \\ & & & \frac{1}{\sigma_n^2} \end{bmatrix}\\ \Delta &=& (A'WA)^{-1}A'Wr \end{eqnarray*}
\sigma_i=1

---
Weighted Least Squares
- Large covariance:
  - Large uncertainty
  - Small weight
  - Large residuals not penalized
  - Outliers have little effect on solution

---
Weighted Least Squares
- Small covariance:
  - High certainty
  - Large weight
  - Large residuals penalized
  - Outliers have significant effect on solution

---
Weighted Least Squares
- Output covariance Cout:
  - Estimate of the accuracy of D
  - Reflection of the Input Covariance C=W-1
  - Can be too large/too small
- Reference variance v:
  - Essentially weighted average of residuals, unitless
  - Cov too big	→ v << 1
  - Cov too small	→ v >> 1
  - Cov just right	→ v ~ 1
\begin{eqnarray*} \Delta &=& (A'WA)^{-1}A'Wr\\ C_\mathrm{out}&=&(A'WA)^{-1}\\ v &=&\frac{r'Wr}{n-\mathrm{dof}} \end{eqnarray*}

---
Outline
- Introduction
  - Least squares for polynomial regression
  - Least squares for Multi-Image Geopositioning (MIG)
  - Improved accuracy with increasing number of images
- Experimental Results
  - Data synthesis, Methodology
  - Results
- Conclusion

---
Multi-Image Geopositioning
- Multiple overhead images see a ground feature
- If we know position/orientation/etc, we can triangulate the location of the ground feature

---
Multi-Image Geopositioning
- Multiple overhead images see a ground feature
- If we know position/orientation/etc, we can triangulate the location of the ground feature

---
Multi-Image Geopositioning
- In reality, position/orientation/etc are imperfect estimates
- Rays do not intersect!
  - Location of ground feature cannot be known certainly
  - Need to find ground point “closest to all” rays

---
Multi-Image Geopositioning
- “Sensor Model” functions map between ground/image
  - Ground-to-image (g2i), Image-to-ground (i2g) are inverses
- Many (infinite) ground points map to each image point
  - Image rays are all (x,y,z) that g2i map to the same (r,c)
  - Equivalent: i2g(r,c,z) for all z
\begin{eqnarray*} (r,c)&=&g2i(x,y,z)\\ & \Leftrightarrow& \\ (x,y)&=&i2g(r,c,z) \end{eqnarray*}

---
Multi-Image Geopositioning
For any ground point

---
Multi-Image Geopositioning
For any ground point
g2i into all images

---
Multi-Image Geopositioning
- For any ground point
  g2i into all images
- Minimize sum of
  squares of image residuals
rc
rr
\Sigma (rr^2+rc^2)

---
Multi-Image Geopositioning
- For any ground point
  g2i into all images
- Minimize sum of
  squares of image errors
- Cov/Weight come from accuracy of measurement
\Sigma \begin{bmatrix}rr_i & rc_i\end{bmatrix} \begin{bmatrix}1/\sigma^2_\mathrm{meas} & 0\\ 0 & 1/\sigma^2_\mathrm{meas}\end{bmatrix} \begin{bmatrix}rr_i \\ rc_i\end{bmatrix} =r'W_\mathrm{meas}r

---
Multi-Image Geopositioning
- Additional weight comes from
  sensor uncertainty
  - What if the camera has a different position/orientation?
  - What would be the spread of g2i?
  - That determines Csens=Wsens-1

---
Multi-Image Geopositioning
Define:
\begin{eqnarray*} r_{(2N\times 1)}&=&\begin{bmatrix}rr_1\\ rc_1\\ \vdots\\ rr_n\\ rc_n\end{bmatrix}\\ W_{(2N\times 2N)}&=&(C_\mathrm{meas} + C_\mathrm{sens})^{-1}\\ A_{(2N\times 3)}&=& \begin{bmatrix} \frac{\partial r_1}{\partial x}& \frac{\partial r_1}{\partial y} & \frac{\partial r_1}{\partial z}\\ \frac{\partial c_1}{\partial x}& \frac{\partial c_1}{\partial y} &\frac{\partial c_1}{\partial z}\\ & \vdots&\\ \frac{\partial r_N}{\partial x}& \frac{\partial r_N}{\partial y} &\frac{\partial r_N}{\partial z}\\ \frac{\partial c_N}{\partial x}& \frac{\partial c_N}{\partial y} &\frac{\partial c_N}{\partial z}\\ \end{bmatrix} \end{eqnarray*}

---
Ground Partial Derivatives
<insert ground partials slides from SM101>

---
Multi-Image Geopositioning
Define:
\begin{eqnarray*} r_{(2N\times 1)}&=&\begin{bmatrix}rr_1\\ rc_1\\ \vdots\\ rr_n\\ rc_n\end{bmatrix}\\ W_{(2N\times 2N)}&=&(C_\mathrm{meas} + C_\mathrm{sens})^{-1}\\ A_{(2N\times 3)}&=& \begin{bmatrix} \frac{\partial r_1}{\partial x}& \frac{\partial r_1}{\partial y} & \frac{\partial r_1}{\partial z}\\ \frac{\partial c_1}{\partial x}& \frac{\partial c_1}{\partial y} &\frac{\partial c_1}{\partial z}\\ & \vdots&\\ \frac{\partial r_N}{\partial x}& \frac{\partial r_N}{\partial y} &\frac{\partial r_N}{\partial z}\\ \frac{\partial c_N}{\partial x}& \frac{\partial c_N}{\partial y} &\frac{\partial c_N}{\partial z}\\ \end{bmatrix} \end{eqnarray*}

---
Multi-Image Geopositioning
- Find the ground point that minimizes: r'Wr
- Iterative, weighted least-
  squares solution:
  - Choose a starting (x,y,z)
  - Use g2i to evaluate residuals r
  - Populate matrix A with partial
    derivatives of g2i
  - Correct (x,y,z) with
    - Dims: (3x2N*2Nx2N*2Nx3)*3x2N*2Nx2N*2Nx1
  - Iterate!
- Output covariance is
- Reference variance is
\Delta = (A'WA)^{-1}A'Wr
C_\mathrm{out}=(A'WA)^{-1}
v=\frac{r'Wr}{N-3}

---
Decomposition
- Note highly block-diagonal form of problem
- Large matrix multiplication/inversion decomposes
  into many 3x3 problems (Only with independent images!)
\begin{eqnarray*} \Delta & = & (A'WA)^{-1} A'Wr \\ & = & \left(\begin{bmatrix}A_1' & A_2' & \ldots & A_N'\end{bmatrix} \begin{bmatrix}W_1 & 0 & & 0\\ 0 & W_2 & \hdots & 0\\ \vdots& & \ddots & \\ 0& & & W_N\end{bmatrix} \begin{bmatrix}A_1 \\A_2 \\ \vdots \\ A_N\end{bmatrix} \right)^{-1} A'Wr \\ & = &\left[ \Sigma_i A_i'W_iA_i \right]^{-1} \begin{bmatrix}A_1' & A_2' & \ldots & A_N'\end{bmatrix} \begin{bmatrix}W_1 & 0 & & 0\\ 0 & W_2 & \hdots & 0\\ \vdots& & \ddots & \\ 0& & & W_N\end{bmatrix} \begin{bmatrix}r_1 \\ r_2 \\ \vdots \\ r_N\end{bmatrix}\\ &=&\left[ \Sigma_i (A_i'W_iA_i) \right]^{-1} \Sigma_i (A_i'W_ir_i) \end{eqnarray*}

---
Output Covariance
- is output covariance (predicted error)
  - Estimate of accuracy of solved answer
  - Depends on measurement sigmas, sensor parameter sigmas, collection geometry
  - Can visualize with “Error Ellipsoid”
    - Diagonal: square-roots (sigmas) are radii along X/Y/Z
    - More general: radii are sqrts of eigenvals along 3 eigenvecs
    - Different scales for different confidence levels
C^{3\times 3}_\mathrm{out}=(A'WA)^{-1}

---
Outline
- Introduction
  - Least squares for polynomial regression
  - Least squares for Multi-Image Geopositioning (MIG)
  - Improved accuracy with increasing number of images
- Experimental Results
  - Data synthesis, Methodology
  - Results
- Conclusion

---
Combining Weight/Covariance
- Start with one nadir ray, image error
- Line of sight is Z axis
- Matrix A (ground partials) is X/Y axes
- With just one ray, the least squares system under-determined!
  - 2 equations, 3 unknowns
C=\begin{bmatrix}\sigma^2 & 0\\0 & \sigma^2\end{bmatrix}; W=\begin{bmatrix}1/\sigma^2 & 0\\0 & 1/\sigma^2\end{bmatrix}

---
Combining Weight/Covariance
- Error “Ellipsoid” is vertical cylinder
\begin{eqnarray*} A'WA &=& \begin{bmatrix}1&0\\0&1\\0&0\end{bmatrix} \begin{bmatrix}1/\sigma^2 &0 \\ 0&1/\sigma^2 \end{bmatrix} \begin{bmatrix}1&0&0\\0&1&0\end{bmatrix}\\ &=&\begin{bmatrix}1/\sigma^2&0&0 \\ 0& 1/\sigma^2 &0 \\ 0&0&0\end{bmatrix}\\ C_\mathrm{out} & = & \begin{bmatrix}\sigma^2&0&0 \\ 0& \sigma^2 &0 \\ 0&0&\infty\end{bmatrix} \end{eqnarray*}

---
Combining Weight/Covariance
- Consider a second image looking along the X axis
- Error “ellipsoid” is horizontal cylinder
\begin{eqnarray*} A'WA &=& \begin{bmatrix}0&0\\1&0\\0&1\end{bmatrix} \begin{bmatrix}1/\sigma^2 &0 \\ 0&1/\sigma^2 \end{bmatrix} \begin{bmatrix}0&1&0\\0&0&1\end{bmatrix}\\ &=&\begin{bmatrix}0&0&0 \\ 0& 1/\sigma^2&0 \\ 0&0& 1/\sigma^2 \\ \end{bmatrix}\\ C_\mathrm{out} & = & \begin{bmatrix}\infty&0&0\\ 0&\sigma^2&0 \\ 0&0& \sigma^2\end{bmatrix} \end{eqnarray*}

---
Combining Weight/Covariance
- Combine both rays in a MIG
- Ellipsoid shape:
  - X and Z radii
  - Y radius
\begin{eqnarray*} \Sigma A_i'W_iA_i&=& \begin{bmatrix}1/\sigma^2&0&0 \\ 0& 1/\sigma^2&0 \\ 0&0& 0 \end{bmatrix} +\begin{bmatrix}0&0&0 \\ 0& 1/\sigma^2&0 \\ 0&0& 1/\sigma^2 \end{bmatrix}\\ &=&\begin{bmatrix}1/\sigma^2&0&0 \\ 0& 2/\sigma^2&0 \\ 0&0& 1/\sigma^2 \end{bmatrix}\\ C_\mathrm{out} & = & \begin{bmatrix}\sigma^2&0&0\\ 0&\sigma^2/2&0 \\ 0&0& \sigma^2\end{bmatrix} \end{eqnarray*}
=\sigma/\sqrt{2}
=\sigma

---
Combining Weight/Covariance
- Add a 3rd ray along Y axis
- Ellipsoid is spherical
  - All radii are
\begin{eqnarray*} \Sigma A_i'W_iA_i&=& \begin{bmatrix}2/\sigma^2&0&0 \\ 0& 2/\sigma^2&0 \\ 0&0& 2/\sigma^2 \end{bmatrix}\\ C_\mathrm{out} & = & \begin{bmatrix}\sigma^2/2&0&0\\ 0&\sigma^2/2&0 \\ 0&0& \sigma^2/2\end{bmatrix} \end{eqnarray*}
\sigma/\sqrt{2}

---
Combining Weight/Covariance
- Each additional ray reduces uncertainty in two directions orthogonal to it
  - Lots of near-nadir images→lots of vertical uncertainty
  - Near-horizontal rays all around→horizontal uncertainty
  - Photogrammetry is mostly overhead→generally more vertical uncertainty
- Calculation of Cout is independent of residuals!
  - Purely a function of relative geometry of rays
  - Refvar measures how well Cout predicts ground accuracy

---
Increasing Number of Images
- In our example, when N increases from 1 to 2:
  - Variance of y decreases:	s2→s2/2
  - Standard deviation of y decreases:	s→s/sqrt(2)
- What about when N=3,4,...?
- What about when geometry is not trivial?
- We will see that accuracy scales as 1/sqrt(N)
  - Law of Large Numbers/Central Limit Theorem
  - Average of N samples has accuracy ~ 1/sqrt(N)

---
Outline
- Introduction
  - Least squares for polynomial regression
  - Least squares for Multi-Image Geopositioning (MIG)
  - Improved accuracy with increasing number of images
- Experimental Results
  - Data synthesis, Methodology
  - Results
- Conclusion

---
Data Synthesis
- Start with 10 overlapping Worldview-1 images
  - 5 stereo pairs, GSD~0.5m
  - Common overlap area includes 36N 117.5W
  - Dolloff, Settergren, ASPRS 2010
- Perturb adjustable parameters (pos, att, vel, etc)
  - 99 variants per original→1000 images
- Choose ground point, project to 1000 image points
  - UTM11N 455000 3984000 1700
  - “Truth” = perfect 1000-image ray intersection
- Further perturb 1000 images
  - Each parameter perturbation randomly sampled Normal with controlled sigma
  - “Error” = 1000 image rays that don't intersect

---
Original 10 Images

---
Data Amplification
- <original 10 look vectors>
- <original 1000 look vectors>
- <perturbed 1000 hi intersections>

---
Methodology
- For N=4...1000
  - For K=1...100
    - Randomly sample subset of N images
    - Compute MIG
      - MIG - truth = measured error
      - Output covariance = predicted error
      - Reference variance = self-consistency check
- Analyze
  - What is the distribution of errors as N grows large?
  - Are reference variances ~ 1?
  - Do measured errors fit predictions (Cout)?

---
Outline
- Introduction
  - Least squares for polynomial regression
  - Least squares for Multi-Image Geopositioning (MIG)
  - Improved accuracy with increasing number of images
- Experimental Results
  - Data synthesis, Methodology
  - Results
- Conclusion

---
Results
- Refvars~1, clustering tighter as N+++
- Predicted error decreasing as N+++
- Horizontal, vertical errors decrease as N+++

---
Average Raw Error
+/- Cancel; very small bias remains

---
Average 3D/Horiz/Vert Error
Decreasing error, Vertical is larger

---
Average 3D/Horiz/Vert Error
Decreasing error, Vertical is larger

---
Reference Variance
Clustered tightly around 1

---
Predicted Error
Larger vertical, two equivalent horizontal

---
Predicted Error * Sqrt(N)
Predicted error decreases like 1/sqrt(N)

---
Measured Error * Sqrt(N)
Measured error decreasing faster than 1/sqrt(N)?

---
Finite Population Error
Measured spread artificially small due to sampling from finite population

---
Finite Population Correction
Standard technique corrects for Finite Population effect

---
Variations
- Increased measurement error
  - Add s=½, 1, 2, 4 pixels of random measurement error
- Variable sensor error
  - Increase all sensor parameter s by a factor of 1--5
- Outer/Inner Cones
  - Sample MIG images from only inner (more vertical)/outer (more oblique) images
- Half/Quarter Cones
  - Sample MIG images from only half (Northern-looking) or quarter (Northeast-looking) images

---
Increased Measurement Error
pix
Reasonable measurement error has little effect

---
Increased Measurement Error
pix
Reasonable measurement error has little effect

---
Variable Sensor error
Ground error larger, but still decreasing

---
Outer/Inner Cones
Narrower cone→More vertical error

---
Outer/Inner Cones
Wider cone→More horizontal error

---
Half/Quarter Cones: Vertical
Narrower cone→More vertical error

---
Half/Quarter Cones: Horizontal
Half→less horizontal error; but Quarter→more?

---
Half/Quarter Cones: Ellipsoid Lean
Quarter: Ellipsoid lean causes 'vertical' error to bleed into horizontal

---
Outline
- Introduction
  - Least squares for polynomial regression
  - Least squares for Multi-Image Geopositioning (MIG)
  - Improved accuracy with increasing number of images
- Experimental Results
  - Data synthesis, Methodology
  - Results
- Conclusion

---
Conclusion
- With N independent images, MIG ground error decreases like 1/sqrt(N)
- Despite many forms of degradation, sufficiently many independent images can still achieve high accuracy